## Slide 1
Smart Parking
IoT Reservation System
Real-time Parking Management with IoT Automation
Presented By
7521955 Davronbek Orifjonov

## Slide 2
Motivation - Urban Parking Challenges
02
30%
of traffic congestion caused by searching for parking
17 min
average wasted per driver finding available spots
$$$
Lost revenue from inefficient space utilization
Traffic Congestion: Aimless circling for parking significantly contributes to urban traffic jams and delays.
Environmental Impact: Increased fuel consumption and carbon emissions from vehicles searching for spots.
User Frustration: High stress levels and wasted time create poor user experiences in city centers.
Lack of Real-time Data: Traditional systems offer no visibility into current availability before arrival.
Inefficient Enforcement: Manual checking of reserved slots is labor-intensive and prone to errors.

## Slide 3
Objectives and Scope
03
Multi-sensor IoT Lock Devices
Integrate magnetic sensor for vehicle detection, battery monitoring, signal tracking, mechanical arm actuator, and tamper alarm into unified units.
Reliable MQTT Communication
Implement MQTT protocol with 4 topic types (up_link, down_link, down_link_ack, heartbeat) for robust bidirectional IoT messaging.
Gateway Coordination Layer
Create gateway devices managing multiple locks with centralized command processing, status aggregation, and health monitoring.
Automated Reservation Lifecycle
Develop complete workflow from slot reservation through vehicle arrival detection to automatic status updates and expiration handling.
Real-time Web Dashboard
Build responsive interface with interactive maps, live status updates via WebSocket, and comprehensive monitoring capabilities.
Data Persistence & Visualization
Implement in-memory storage with system logs, sensor data tracking, and reservation management for operational visibility.

## Slide 6
Data Model
06
Core Entities
Parking Lots
idUUID (PK)
nameString
addressString
coordinates{lat, lng}
total_slotsInteger
availableInteger
Parking Slots
idUUID (PK)
lot_idUUID (FK)
gateway_idString
statusEnum(free/occ...)
batteryInteger (%)
signalInteger (dBm)
Reservations
idUUID (PK)
slot_idUUID (FK)
plate_numString
user_infoJSON
timespan{start, end}
statusEnum
System Logs
idUUID (PK)
typeString
levelEnum(info/err)
messageText
timestampDateTime
metaJSON
Relationships
Lot
Slots
Gateway
Locks
Slot
Active Res
Status changes trigger automatic cascades (e.g., Expiration → Slot Release)
One-to-Many
One-to-Many
One-to-One

## Slide 7
Data Flow
07
Real-time Pipeline
MQTT Topics
Structure: /{gateway_id}/{type}
.../up_link
Status Upd
.../down_link
Commands
.../down_link_ack
Confirm
.../heartbeat
Health
{ deviceId, timestamp, sensors... }
Reservation Lifecycle
System Logic
Server-side Check (30s)
Scans active reservations. If now > endTime, mark expired & release slot.
Device Self-Check (10s)
Lock verifies reservation validity locally. Auto-release if connection lost/timeout.
Bidirectional Flow
Commands (Server → Gateway)
Status (Gateway → Server)
JSON Payload
MQTT (TCP)
Sub / Pub
WebSocket
Reserve: User books slot via App/Web
Command: Server publishes 'reserve'
Actuate: Gateway raises Lock Arm ⬆️
Arrival: User arrives, Arm lowers ⬇️
Detect: Magnetic sensor sees vehicle
Update: Status: Occupied
Gateway
Publishes State
Broker
Routes Msg
Web Server
Process Logic
Dashboard
Live UI

## Slide 8
Device Simulation (Node.js)
08
Edge Device 1: Parking Lock
Sensors
Magnetic
> 500 units
Battery
70-100%
Signal (RF)
0-100%
Actuators
Mech. Arm
Raise/Lower (2s)
Speaker
Tamper Alarm
State Flow
Edge Device 2: Gateway
Responsibilities
Coordinators for 3 locks per gateway
MQTT Connectivity (TCP/IP)
Command Processing & Routing
Status Aggregation
Topology
Simulated Hardware Unit
Coordinator Node
Heartbeat: 30s
ACK System
Free
Reserved
Occupied
Free

## Slide 10
Backend API (Express.js)
10
Core Endpoints
Method | Endpoint Route | Purpose
GET | /api/parking-lots | List all lots with availability summary
GET | /api/parking-slots?lot_id={id} | Get specific slots & status for a lot
POST | /api/reservations | Create new slot reservation
GET | /api/reservations?filter=active | List current user's active bookings
POST | /api/reservations/:id/arrive | Mark arrival trigger (Opens Lock)
DEL | /api/reservations/:id | Cancel existing reservation
GET | /api/dashboard-stats | Real-time system statistics
GET | /api/system-logs?limit=50 | Recent audit and system event logs

## Slide 11
Dashboard Features
11
5-Tab Interface Structure
Dashboard
Live statistics (Total, Available, Occupied, Reserved)
DEFAULT
Map View
Interactive Leaflet map with color-coded markers
Parking
Browse lots and select specific available slots
Reservations
Manage active bookings & "I'm Here" arrival trigger
Monitoring
Real-time System logs and MQTT message tracking
Real-time Updates
WebSocket Connection
Instant state reflection via Socket.IO
Toast Notifications
Alerts for "Vehicle Detected" or "Confirmed"
Auto-Refresh
Dynamic slot availability without page reload
Responsive & Interactive
Mobile-First Design
Touch-optimized controls for smartphones
Visual Indicators
Green/Red/Yellow status color coding
Geolocation
"Find Nearby" using browser GPS API

## Slide 13
Live Demo — Flow
13
Demonstration Timeline
1
System Init
Start MQTT Broker 1883
Launch Web Server 3000
Connect 2 Gateways (6 Locks)
Dashboard auto-launch
2
Booking Flow
Select Downtown Lot A
Click Green Slot
Enter: ABC-123 / 2h
Lock Arm Raises ⬆️
3
Park Vehicle
Click "I'm Here" button
Lock Arm Lowers ⬇️
Magnetic Sensor Detects
Status: Occupied
4
Real-time Data
Stream MQTT Messages
Battery & Signal stats
Heartbeat (30s interval)
Departure → Free
Startup
30 Sec
Reserve
1 Min
Arrival
1 Min
Monitor
30 Sec

## Slide 14
Achievements & Takeaways
14
DONE
Integrated IoT Pipeline
Successfully connected 2 distinct device types (Locks + Gateways) establishing a robust edge-to-cloud data path.
DONE
Real-time Monitoring
Implemented low-latency communication using MQTT for devices and WebSocket dual-channel for the dashboard.
DONE
Automated Enforcement
Developed autonomous logic for slot enforcement with physical lock simulation covering 4 distinct mechanical states.
DONE
Complete Lifecycle
Engineered end-to-end workflow handling booking, arrival detection, parking duration, and auto-release upon departure.
DONE
100% Compliance
Met all functional requirements including multi-sensor integration, interactive dashboard, and system visualization.
DONE
Modular Architecture
Built a scalable, component-based system design that decouples device simulation from backend logic, ready for production.

## Slide 15
Future Directions
15
Q2 2026
Phase 2: Expansion
License Plate Recognition
OpenALPR + Camera Integration
Native Mobile App
React Native (iOS/Android)
Payment Gateway
Secure Stripe Integration
Database Migration
PostgreSQL Persistent Storage
Q3 2026
Phase 3: Intelligence
ML Predictions
Occupancy Forecasting Models
GPS Auto-Arrival
Geofencing Detection Logic
Multi-Tenant Support
White-label SaaS Solution
Cloud Deployment
AWS IoT Core + Lambda
INFRASTRUCTURE
Hardware Integration
LoRaWAN Devices
Replace simulated locks with real IoT hardware
Physical Sensors
Deploy vehicle detection loops & magnetometers
RF Communication
Implement 433 MHz protocol (Gateway ↔ Locks)

## Slide 16
IoT Automation Project 2026
Questions?
Thank You!
Smart Parking IoT Reservation System
7521955 Davronbek Orifjonov